## Slide 1
PDMS11.2
New Bolting
Training
Paragon/Specon
CADCENTRE
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: 11.2 Bolting
The New Features
The New Hierarchy
The Elements used for New Bolting
New Attributes
The Calculation Process
Specification Set-up
Mixed Bolt Sets Example
Further Selectors
Additional Information

## Slide 3: The New Features
Mixed Bolt Sets for the same Joint
Jacking Screws
Cap Screws
Additional MTO items for Nuts, Washers, Isolators and Locking nuts
Separate Bolt Specs
Correct Bolt length calculations at Nozzles

## Slide 4: The New Hierarchy

## Slide 5: The Elements used for New Bolting
BTSE (Bolt Set) - Administrative element, one required for each joint with differing bolt requirements
BLTP (Bolt Point) - The actual bolt, one required for each bolt hole within a flange at the given joint
BLTAB (Bolt table) - Administrative element for version 10.5 that owns elements still used in 11.2 bolting
BLIST (Bolt List) - Secondary administrative element for version 10.5 that owns SBOL’s still referenced to in 11.2
SBOL (Single Bolt Set) - Element used at version 10.5, now holds information about extra lengths, items and is the link to the DTAB element
LTAB (Length Table) - Secondary administrative element that existed at version 10.5 owns DTAB elements used in 11.2
DTAB (diameter table) - Existed at version 10.5, contains information about standard bolt lengths

## Slide 6: Referencing Bolt Set
<footer>
<date/time>
BTSE referenced by component through new attribute BLRF (Bolt Reference array)
If component has same bolting requirement for each connection, a single entry in BLRF is sufficient.
If connection requirements are different at connecting points then an entry of each connection is required. Maximum 10 entries.

## Slide 7: New Element BLTP
BLTP (Bolt Point) - the bolt - stores bolting information for the individual bolt
BLTP attributes
  NUMB (Number) - Bolt hole number in the flange, must match mating BLTP answers
  * BDIA (Bolt diameter) - Diameter of the bolt required, must match mating BLTP answers
  * BTHK (Bolt Thickness) - Bolt length required through the flange thickness
  * BTYPE (Bolt Type) - Type of Bolt required, to be answered with one of the following:-
    BOLT (Generic Bolt - Default), MACH (Machine Bolt), STUD (Stud Bolt), CAP (Cap Screw), JACK (Jacking Screw) or TAP (Tapped Hole)
*Can reference the SCOM parameter or be a fixed value

## Slide 8: Example syntax setting BLTP Attributes
NUMB value NUMB 1 NOTE: each BLTP must have a different number within the set and be numbered in order
BDIA value BDIA 1/2 BDIA (1/2IN) BDIA (PARA[2])
BTYP word BTYP STUD
BTHK value BTHK 1 BTHK (1/2IN) BTHK PA 2 BTHK SUM PA2 3/4 BTHK (PARA[2] + 3/4IN)
BTHK can not be set to a number less that 0.6

## Slide 9: New Attributes
The Various Settings for the BTHK attribute at a BLTP
Can also be answered using a Mathematical expression or setting to Zero
Components with blind holes have the tapping depth
assigned to their BTHK
Jacking bolts have their BTHK answer for that BLTP set to the sum of the flange/facing thickness and the req’d opening gap
Wafer components with no bolting do not require a Bolt Pointset reference
Wafer components with special bolting needs require a BTHK answer for the specific BLTPs affected

## Slide 10: New Attributes
BTYPE answer Pecking order
3 BOLT
Priority 1 will overwrite
Priority 2 & 3 answers, 2 MACH
Priority 2 will overwrite STUD
Priority 3 answers only
CAP
1 JACK
TAP

## Slide 11: SBOLT Attributes
SBOLT attributes for use in New Bolting
  NSTD (Non-Standard) - A reference attribute to the DTAB
  ** BITEM (Bolt Items) - Additional bolt items that can be used to output separate MTO information for nuts, washers, etc*
  ** BITL (Bolt Item Lengths) - The lengths of the additional bolt items*
  ** XTRA (Extra) - The length allowed for extension thread
DTAB attribute for use in New Bolting
  BLEN (Bolt Lengths) - Standard ordering lengths for a particular bolt size*
*These are Array attributes and are not linked together
** New Attributes

## Slide 12
Additional Bolting Items

## Slide 13: Additional Bolting Items
Each type of bolt can have further items associated with it, such as washers, nuts, locking nuts and isolation tubes.
SBOLTS have the attribute BITEMS, which is a word array up to ten elements, which represents a BTYP selector for additional bolt SPCOM’s in the Bolt Specification, such as NUT, LNUT, WASH or ISOL. Specified words of a maximum of 4 alpha characters.
This generates a further selection of material from the
Bolt Specification.

## Slide 14
SBOL /I-NN-D
Nstdblength /5/8
Bdiameter
Length SBOLT attributes not required to be set for new
Noff bolting
Xtralength 3/16 Extension thread length
Bitems NUT WASH WASH NUT Bolt item BTYPs
Bitlength 19/32 1/16 1/16 19/32 Bolt item lengths
Additional Bolting Items
The SBOL now includes additional bolting items

## Slide 15: The Calculation Process

## Slide 16: The Calculation Process

## Slide 17: The Calculation Process

## Slide 18: The Calculation Process

## Slide 19: Specifications Set-up
Pipe Specifications have a reference attribute BSPEC, which
can be set to a specification containing bolts.
Bolts will be selected from the Bolt Specification (BSPEC) if set, or from the Piping Specification of the flanged component if not.
To indicate the method of bolting the attribute BLTM must be set to text string |NEW|.

## Slide 20
HEADING
TYPE NAME PBOR0 STYP SHOP CATREF DETAIL MATXT CMPREF BLTREF
DEFAULTS
- - - WN TRUE
FLAN */FW-LV-3 3.00 WN TRUE /FLAN-WNLV-80 /FL-WN-LV /A40 =0 =0
HEADING
TYPE NAME PBOR0 STYP SHOP CATREF DETAIL MATXT CMPREF BLTREF
DEFAULTS
- - - RF FALS
GASK */GC3 3.00 RF FALS /ACGCBDTLL /GASK.300.RF.1/16 =0 =0 =0
HEADING
TYPE NAME PBOR0 STYP SHOP CATREF DETAIL MATXT CMPREF BLTREF
DEFAULTS
- - - GATE =
VALV */VLUG3 3.00 BFLY FALS /A0VFWDALL /A0VFWDA-D /DUM-MT =0 =0
VALV */VGATE 3.00 GATE FALS /AAVGBDRLL /AAVGBDR-D /DUM-MT =0 =0
HEADING
TYPE NAME BDIA BTYP CATREF DETAIL MATXT CMPREF BLTREF
DEFAULTS
- - - STUD
BOLT */BOLT-S:5/8 0.5/8 STUD /BOLT /STUD-D /MAT-BOLT =0 /SBOL-STUD-5/8
BOLT */BOLT-C:5/8 0.5/8 CAP /CAP /CAP-D /MAT-CAP =0 /SBOL-CAP-5/8
BOLT */BOLT-W:5/8 0.5/8 WASH /WASH /WASH-D /MAT-WASH =0 =0
BOLT */BOLT-N:5/8 0.5/8 NUT /NUT /NUT-D /MAT-NUT =0 =0
The Specification

## Slide 21: Bolt Selection From Specification
If the BTYP of the bolt point for both sides of joint is set to BOLT, the default bolt in the specification is used.
If the BTYP of the bolt point for one side is set to BOLT, and the other is set to anything other than BOLT, then the type of bolt specified by that BTYP will be used.
If both BTYP’s are the same and not set to BOLT, the bolt with that BTYP will be selected.
If the BTYP’s are not equal and are also not set to BOLT, the “upstream” component’s BTYP is selected.

## Slide 22: Bolt Selection From Specification
If a bolted through flange has its BTYP set to BOLT,
and its mating flange may require cap screws and has its BTYP set to CAP. In this instance, the CAP screw overrides the default type, and the BTYP of the bolt for selection will be CAP.
If inconsistent combinations of bolt path data are found for a particular bolt, an error message is output for that joint, but detailing will continue.

## Slide 23
Through Bolts
Caps
Mixed Bolt Sets Example/Exercise

## Slide 24
Required Output

## Slide 25
Flange - The flange has the attributes
BLTP members 1..8
Param 76.2 79.37 FBD BWD 28 89 210 117 25
Blrfarray /WNLP-3
BTSE /WNLP-3
Number 1..8
Bdiameter 5/8in
Btype BOLT
Bthkness PARAM 5
28

## Slide 26
Valve- The wafer valve has the attributes
The BTSE has 8 BLTP members 4 through bolts, 4 caps
BLTP members 1,3,5,7
Param 76.2 19.05 WGWD 203 105 254
Blrfarray /BTSE-WAFER-LUG
BTSE /BTSE-WAFER-LUG
Number 1 (3 5 and 7)
Bdiameter 5/8
Btype BOLT
Bthkness 0
BLTP members 2,4,6,8
Number 2 (4 6 and 8)
Bdiameter 5/8
Btype CAP
Bthkness (1/8in)

## Slide 27
P1
P2
BLTP members1,3,5,7
Btype BOLT Bthkness 0
1.1/2”
BLTP members 2,4,6,8
Btype CAP Bthkness (1/8in)

## Slide 28: General Wafer Components
The calculation of bolts through wafer components is the
same as the standard flange - gasket - flange calculation,
with following differences.
If within the joint, a component’s connection type starts with W (wafer) and G (Gaskets) , get its P1 - P2 distance, and go to the next component.
The joint may contain any number of wafer components, (for example, butterfly valves, orifice plates, spectacle plates, spades) and any number of gaskets. The total bolted through length will be summed and added to the flange thicknesses.

## Slide 29: Further Selectors
In addition to Bolt Specific Type and Diameter, a further degree of bolt selection is allowed via the BSEL
selector in the Bolt Specification.
e.g. If the Pipe Specification dictates that the same flange has black bolts indoors and galvanised bolts outdoors, then BSEL could be set to either IN or OUT at the flange, with entries for both bolts in the Bolt Specification.

## Slide 30
HEADING
TYPE NAME BDIA BTYP BSEL CATREF DETAIL MATXT CMPREF BLTREF
DEFAULTS
- - - STUD =
BOLT */BOLT-S:5/8 0.5/8 STUD IN /BOLT /STUD-D /MAT-BOLT =0 /SBOL-STUD-5/8
BOLT */BOLT-S:5/8 0.5/8 STUD OUT /BOLT /STUD-D /MAT-BOLT-OUT =0 /SBOL-STUD-5/8
BOLT */BOLT-C:5/8 0.5/8 CAP IN /CAP /CAP-D /MAT-CAP =0 /SBOL-CAP-5/8
BOLT */BOLT-C:5/8 0.5/8 CAP OUT /CAP /CAP-D /MAT-CAP-OUT =0 /SBOL-CAP-5/8
BOLT */BOLT-W:5/8 0.5/8 WASH IN /WASH /WASH-D /MAT-WASH =0 =0
BOLT */BOLT-W:5/8 0.5/8 WASH OUT /WASH /WASH-D /MAT-WASH-OUT =0 =0
BOLT */BOLT-N:5/8 0.5/8 NUT IN /NUT /NUT-D /MAT-NUT =0 =0
BOLT */BOLT-N:5/8 0.5/8 NUT OUT /NUT /NUT-D /MAT-NUT-OUT =0 =0
Further Selectors

## Slide 31: Additional Information
Bolting across Specification breaks:
  Bolts will be selected from the second Specification if they cannot be selected from the first Specification
  The first Specification is defined as the gasket Specification if a gasket is present, otherwise it is defined as the downstream component Specification
In the event that bolts are included in vendor supply, I.e. An orifice flange assembly, a null BLTREF of the CATREF indicates that no bolts will be output for that joint

## Slide 32: Additional Information
Bolt Lengths at Nozzles
Nozzle flanges are handled exactly as other flanges,
via a BLRF of CATREF
This provides an accurate calculation ensuring that the correct bolt lengths are calculated even when nozzles use special flanges